## Slide 1: Network Security
Part 2: protocols and systems (d) Security in wide-area wireless networks

## Slide 2: Security in wireless mobile networks
Wireless mobile networks have characteristics that warrant special attention, in particular when dealing with security issues
  Transmission medium
    The air interface, by definition, is much more open to passive security attacks than wired media
    Active attacks are a little more difficult to mount, but still way easier than on a wired medium
    Reduced bandwidth capability, and increased latency wrt. wired media: this calls for “light” protocols, both in terms of number of exchanged messages and in terms of the amount of data exchanged
    Authentication becomes a crucial concern, even in controlled environments (such as corporate networks)
  Mobility of user devices
    User mobility requires that security mechanisms be particularly fast and efficient (e.g., to support real-time handoffs)
  Type of user devices
    Wireless devices often have limited computational power, memory, etc.: security protocol design for these networks must take these factors in account
So far there has been a tendency to adapt to the mobile/wireless case security mechanisms that were designed for wired networks: unfortunately, this works less often than we would like…
On this topic we will see:
  Authentication in GSM (2G) networks
  Authentication in UMTS/LTE (3/4G) networks
  How things should change with 5G
Notes: Global System for Mobile Communications: first deployed in Finland (Telecom Finland) in December 1991
Universal Mobile Telecommunications System: first deployed in UK in 2003 by “3”
Subscriber Identity Module

## Slide 3: Security (authentication) in 1G
Notes: GSM, sigla di Global System for Mobile Communications

## Slide 4: Security in 1G
This slide is intentionally left blank...
Notes: TACS, acronimo di Total Access Communication System (in italiano sistema di comunicazione ad accesso totale) è uno standardanalogico di telefonia mobile di prima generazione sviluppato negli anni ottanta del XX secolo
mid 80, 2005
Trasmissione analogica con FDM

## Slide 5: Security (authentication) in GSM/2G
Notes: GSM, sigla di Global System for Mobile Communications

## Slide 6: GSM: reference architecture (simplified)
MS: Mobile System
HLR: Home Location Register
VLR: Visiting Location Register
AuC: Authentication Center
BTS: Base Transceiver Station
BSC: Base Station Controller
SIM: Subscriber Identity Module
MSC: Mobile Switching Center
EIR: Equipment Identity Register
BTS
BTS
BSC
Uu
MS
Radio Access
Network
Home
Central Office
Visited
Central Office
MSC/VLR
Signaling
Data path
EIR
SS7
Network
PSTN
Network
HLR/AuC
Notes: SS7, anche noto come Signaling System #7, è un set standardizzato di protocolli di segnalazione usati nelle reti telefoniche PSTN (Public Switched Telephone Network) mondiali per gestire le chiamate.
2017 era il più diffuso al mondo con più di 3 miliardi di persone in 200 Stati
GSM = Groupe Spécial Mobile
standard si basa sull'algoritmo sviluppato da Andrew Viterbi di codifica delle trasmissioni digitali
1987: Specifiche definite da un accordo tra 13 paesi EUROPEI
1989: ETSI pubblica le specifiche in un libro di 6000 pagine
La prima telefonata GSM su rete commerciale avvenne nel 1991, tra l'allora primo ministro finlandese Harri Holkeri e Kaarina Suonio vice sindaco della città di Tampere. La prima rete GSM fu costruita da Telenokia e Siemens – l'odierna Nokia Networks – per conto dell'operatore finlandese Radiolinja oggi Elisa Oyj.
In Italy first service starts in 1992 by SIP, now TIM

## Slide 7: GSM: authentication protocol
Goals
  Authentication is one-way: network authenticates user, not vice-versa
  Ephemeral keys derivation
  Keep MS’ identity hidden, when possible (see UMTS case)
Authentication credentials:
  IMSI (International Mobile Subscriber Identity), Ki
    Stored in SIM
    There should be no APIs to read Ki from SIM
  IMEI (International Mobile Equipment Identity)
    Numeric ID of the terminal, not SIM
In addition, the SIM stores other data and algorithms used for authentication and security in GSM:
  A3: auth. algorithm
  A5: confidentiality
  A8: key-generation
In addition to cryptographic authentication, based on credentials stored in the SIM, GSM can check the status of a mobile terminal, identified by its IMEI
  EIR can identify a given IMEI as white (MS OK), grey (MS is “under observation”), black (e.g., stolen MS)
Notes: IMSI è la sigla di International Mobile Subscriber Identity. Ki chiave usata per calcolare la SRES dato il RAND
EIR: Equipment Identity Register
GSM, sigla di Global System for Mobile Communications

## Slide 8: GSM authentication protocol (simplified)
The Authentication Vector [AV] (message 2) includes n vectors: VLR can execute n different authentication runs with the client without re-connecting to the HLR
  Each i-th vector includes
    RAND: challenge to the client
    SRES: expected response
    Kc: ephemeral key, used by algorithm A5 to provide confidentiality over the air
RAND (message 3) serves as the challenge from the network to the client
At step (C) the network authenticates the client: the client proves it (the SIM) knows Ki, by calculating the correct RES
MS
MSC/VLR
HLR/AuC
Sec. Information RQST
Sec. Info. RESP (AV x n)
Auth. RQST (RANDi)
Auth. RESP (RES)
1
Store AV1, …, AVn
Select i
2
3
4
Compute SRES, Kc
Verify RES=SRESi
Generate n AVs
A
B
C
Notes: Ki chiave usata per calcolare la SRES dato il RAND
Pacchetto 1 include la IMSI (International Mobile Subscriber Identity)

## Slide 9: GSM: AuC and MS, steps (A) and (B)
AuC keeps a database of all registered users, keyed by IMSI
VLR includes MS’ IMSI in “security information RQST” (message 1)
A3-A8: MAC algorithms, with Ki as key
  The GSM consortium felt the need to “invent” their own MACs, so A3 and A8 are not (supposed to be) published, well-known algorithms (see later…)
AuC generates n vectors, composed by [RAND,SRES,Kc]i tuples, 1≤i≤n, and sends them to VLR in message 2
MS computes RES and Kc using the same methods, and sends RES to VLR in message 4
Generate Random Number (RAND)
128 bit
SRES
32 bit
A3
Kc
64 bit
A8
Ki 128 bit
Notes: AuC: Authentication Center
VLR: Visiting Location Register

## Slide 10: GSM: VLR, step (C)
The VLR chooses one of the tuples contained in the Authentication Vector, and sends the corresponding RANDi to MS (message 3)
The VLR checks the validity of MS’ RES (RES := SRESi), and thus authenticates MS
The VLR can perform other re-authentication rounds, using one of the other n-1 tuples contained in the Authentication Vector
  This kind of re-authentication procedure (not involving the AuC) can be used when MS moves between one VLR and the next
Note: to avoid replay attacks, the same value of RANDi cannot be reused

## Slide 11: GSM: cryptographic algorithms
A3: authentication
  It runs end-to-end between AuC and MS: it can be chosen by each operator independently. Why??!?!
  It was initially based on an algorithm known as COMP128
  Successfully cryptanalyzed in 1998: known to be vulnerable to chosen-text (chosen-challenge) attacks that allow the attacker to get the MS’ SIM to reveal Ki
    Once Ki is known, it is trivial with a passive attack to compute Kc, breaking confidentiality
  Two ways of mounting the attack
    Gaining physical access to the SIM (think about phone resellers)
    Over the air: planting a fake GSM base station somewhere (thanks to one-way authentication, MS will not discriminate between fake and real BTS’). Note that this is illegal in most (probably all) countries
A5: confidentiality
  It must be the same between all operators that implement roaming agreements. Why2??!?!
  Stream cipher
  Even the strongest variant (A5/1) has been successfully cryptanalyzed in 1998/99: it is possible to recover Kc with a passive attack over the air, assuming one stays with the same BTS for a very long time
  However, this attack is actually not very practical to implement
A8: key-generation
  Same considerations as with A3

## Slide 12: Security in GSM networks: summary
From a design standpoint, the security architecture of GSM has proven to be a significant failure. Main issues:
  Design and use of cryptographic algorithms should be left to cryptographers
  Security by obscurity never works: will engineers ever learn?
Cryptographic mechanisms protect data only over the air (MS - BSC)
  Without additional countermeasures attacks are always possible on the terrestrial side of the network
  The security on the terrestrial side of the network is based on the fact that the network is “closed”, unlike, e.g., an operator’s IP backbone
Besides the weaknesses of the cryptographic algorithms, key length chosen by the GSM designers is also an issue
  E.g., Kc is only 64 bit long (but at least Kc is ephemeral…)
Last, but not least, authentication is not mutual
  Practically this could be a relatively small issue if we are talking about pure GSM networks (see legality issues related to planting a fake GSM base station…)
  However, this becomes a real issue (i.e., attacks become really practical) when the same SIM is reused in different, non-GSM, networks, such as 802.11
  Note also that today for as low as 300$ you can create your own RAN broadcasting fake networks
    See OpenBTS project, http://openbts.org/w/index.php/Main_Page (old wiki @ http://wush.net/trac/rangepublic)

## Slide 13: Authentication and security in UMTS/LTE

## Slide 14: UMTS: reference architecture (simplified) LTE: security very similar (check terms however)
MS: Mobile System
HLR: Home Location Register
VLR: Visiting Location Register
AuC: Authentication Center
H-AAA: Home AAA
F-AAA: Foreign AAA
SGSN: Serving GPRS Support Node
GGSN: Gateway GPRS Support Node
RNC: Radio Network Controller
HA (FA): Home (Foreign) Agent
PS/CS: Packet Switched (service), Circuit Switched (service)
USIM: User Services Identity Module
Node-B
Node-B
RNC
Uu
MS
SGSN
GGSN
H-AAA
HA
Radio Access
Network
F-AAA
Home
Central Office
Visited
Central Office
HLR/AuC
MSC/VLR
Signaling
Data path
EIR
Internet
SS7
Network
PSTN
Network
Notes: Universal Mobile Telecommunications System
Universal Subscriber Identity Module
EIR: Equipment Identity Register
MSC: Mobile Switching Center
General Packet Radio Service: È stato il primo sistema cellulare progettato specificamente per realizzare un trasferimento dati a commutazione di pacchetto e a media velocità su rete cellulare per agganciarsi alla rete Internet, usando i canali TDMA della rete GSM. In un primo momento la definizione di tali specifiche era demandata all'ETSI, mentre attualmente è affidata al Comitato 3GPP (3rd generation partnership project)
Enhanced Data rates for GSM Evolution
1998 3GPP 3rd Generation Partnership Project is founded, services start after 2003

## Slide 15: UMTS/LTE: Authentication and Key Agreement (AKA)
MS
SGSN/VLR
MSC/VLR
Mutual authentication protocol
  Based on ISO/IEC 9798-4
Active entities are MS, VLR (SGSN for Packet Switched mode, MSC for Circuit Switched mode), and HLR/AuC
Goals
  Mutual authentication between MS and network
  Setup of ephemeral keys, for integrity protection and to provide confidentiality
  Protection of confidentiality, in case of passive attacks, of:
    Position of MS
    Active network services (voice, data, etc.)
    IMSI, when possible
      Messages (1) and (2) are exchanged only when MS’ IMSI is not already in the VLR’s database, otherwise TMSI is used
HLR/AuC
Attach RQST
Identity RQST
Identity RESP
AKA
AKA
Location update
Attach accept
Attach complete
UMTS attach procedure
(simplified)
1
2
Notes: Serving GPRS Support Node
Gateway GPRS Support Node
MSC: Mobile Switching Center

## Slide 16: Authentication in UMTS/LTE: main elements
MS’ credentials, stored in USIM
  International Mobile Subscriber Identity (IMSI)
    FIXED, can be read from USIM
  Temporary Mobile Subscriber Identity (TMSI)
    Assigned by nework when connecting and authenticating using IMSI
    Used during following connections/authentication unless errors that require to revert using IMSI
    Can be read from USIM
  Packet Temporary Mobile Subscriber Identity (P-TMSI) (same as TMSI)
Cryptographic credentials
  K: pre-shared key, known to AuC and USIM
    FIXED, cannot be read from USIM
Cryptographic algorithms f1-f5, f8-f9
  Unlike GSM algorithms have been published and publicly analyzed before being standardized
AS we will see the major vulnerability of the system is in TMSI/IMSI management

## Slide 17: Authentication with AKA in UMTS/LTE
Message (1) carries the MS’ IMSI, allowing AuC to identify the terminal
The Authentication Vector (AV) carried in message (2) contains n authentication tuples, similarly to GSM
  Each i-th tuple includes:
    XRES: Expected Response
    AUTN: the value that allows the MS to authenticate the network
    Ephemeral keys
In message (3)
  RAND serves as a challenge from the network to the MS
  AUTN serves as authentication response from the network to the MS
At step (B) the MS authenticates the network
At step (C) the network authenticates the MS
MS
SGSN/VLR
MSC/VLR
HLR/AuC
Auth. Data RQST
Auth. Data RESP (AV x n)
Auth. RQST (RANDi, AUTNi)
Auth. RESP (RES)
1
Store AV1, …, AVn
Select i
2
3
4
Compute RES, XMAC
Verify AUTN
Verify RESi
Generate n AVs
A
B
C
Notes: AuC Authentication Center

## Slide 18: AKA: AuC, step (A)
AuC finds in its database, keyed by IMSI, the following parameters:
  K: the pre-shared key for this IMSI
  SQN: the current valid sequence number for this IMSI
f1-f5: MAC algorithms with K as secret parameter
  These are used also as ephemeral key generators
AMF: Authentication and key Management Field
  It handles special cases, such as selection of algorithms other than the standard ones, etc.
SQNuser := SQNuser + 1
Generate Random Number (RAND)
XRES
(Expected
Response)
32-128 bit
f2
CK
(Cipher
Key)
128 bit
f3
IK
(Integrity
Key)
128 bit
f4
AK
(Anonymity
Key)
f5
MAC
(64 bit)
f1
AMF 16 bit
48 bit
K (128 bit)
128 bit
AVi = [RAND | XRES | CK | IK | AUTN]
AUTN = [AK⊕SQN | AMF | MAC]

## Slide 19: AKA: AuC, step (A) - continued
SQN: sequence number
  Sequence numbers are an alternative to nonces in authentication protocols: they represent “implicit nonces” from the MS to AuC
    The MS will accept AUTN iff its derived from a valid (fresh) SQN
  It guarantees the freshness of parameters and protects from replay attacks, minimizing the number of round-trips required to carry out the protocol run
  However, it requires to be kept in sync between MS and AuC: both have to store the last values used as SQN
  Synchronization procedures are usually expensive in terms of how many roundtrips are needed
AK: protects SQN from passive attacks
  By looking at how the value of SQN changes over time, an attacker could derive information about the position and/or the identity of a user

## Slide 20: AKA: MS, step (B)
Besides checking the validity of XMAC, MS must also verify that SQN is valid
  USIM stores the last value of SQN used by the network
  Usually SQN values that differ from the expected value by one or two are allowed, taking into account lost packets, and avoiding, if possible, the expensive re-synchronization procedure
If XMAC is not valid, MS does not send RES
  This should solve any problem due to known-text attacks (see the GSM case)
All these algorithms are run inside the USIM, not inside the MS
RES
f2
CK
f3
IK
f4
AK
f5
XMAC
f1
K (128 bit)
RAND
AUTN = [ AMF | AK⊕SQN | MAC]
SQN
RAND
Verify MAC=XMAC
Verify SQN in correct range
⊕

## Slide 21: AKA: VLR, step (C)
VLR must check the validity of RES: RES := XRESi
As in GSM, since the Authentication Vector contains several authentication tuples, the VLR can run several AKA runs without contacting the AuC again
As in GSM, each value RANDi can be used only once
  Once the n tuples have been used, the VLR will have to execute a run with the HLR/AuC to get a new AV, in case it needs to re-authenticate the MS

## Slide 22: UMTS: confidentiality, both for user data and signaling
COUNT-C - A simple way to make sure that the same keystream isn’t generated more than once. Its value depends on several radio-level parameters
BearerID - Identifies a particular channel between MS and RNC. Prevents the same keystream to be generated for more than a bearer channel between MS and RNC
Direction - Generate different keystreams for the uplink and downlink
Length - Specifies the length of each keystream blocks
f8
CK
Length (16 bit)
COUNT-C
BearerID
(5 bit)
Direction (1bit)
Plaintext block
Keystream block
Ciphertext
f8
CK
Keystream block
Length
BearerID
Direction
COUNT-C
Plaintext block
Sender: MS (RNC)
Receiver: RNC (MS)
Notes: A bearer service is a link between two points, which is defined by a certain set of characteristics.

## Slide 23: UMTS: integrity, both for user data and signaling
f9
IK
FRESH
COUNT-I
Message
Direction (1bit)
f9
IK
Sender: MS (RNC)
Receiver: RNC (MS)
FRESH
COUNT-I
Message
Direction (1bit)
MAC-I (XMAC-I)
XMAC-I (MAC-I)
COUNT-I - See COUNT-C
Message - The message to be integrity-protected
Direction - See previous slide
FRESH - A nonce that the network sends to MS before beginning ciphering. Its value changes every time an MS performs an Attach procedure. It prevents an MS (network) from reusing the same integrity codes twice (replay attack)

## Slide 24: UMTS: the Kasumi algorithm
Kasumi is a simmetric block cipher
  Block size is 64 bit
  Based on a Feistel-like scheme with eight rounds
Both f8 and f9 are based on Kasumi
Patented by Mitsubishi
To date it has been extensively cryptanalyzed, without finding any significant flaws

## Slide 25: Security in UMTS/LTE
“Security by obscurity” replaced by “security by expert design”
Authentication protocol, ciphering suite and the type of security credentials have been designed specifically for the wireless environment
  For example, avoid the use of asymmetric cryptography
  Not necessarily good for environments other than 3G UMTS, though (e.g., authentication protocol requires re-synchronization in certain cases, might be too inefficient for low-bandwidth/high-latency links)
Once again, security in the terrestrial part of the network is left to “keeping its boundaries secure”

## Slide 26: Simple vulnerabilities in 2/3/4G and bug fixes with 5G

## Slide 27: Security in UMTS/LTE: problems with TMSI
While cryptographically secure, UMTS/LTE exhibit vulnerability with TMSI
  Attackers can easily force mobile nodes in exposing their real IMSIs
Basic recipe:
  1) set up a rogue eNB posing as user’s network
  2) force MS disconnecting from network using jammer
  3) wait for MS to re-connect to rogue eNB
  4) capture IMSI and disappear
MS
rogue
eNB
eNB
MS
rogue
eNB
eNB
jamming
LTE

## Slide 28: Security in UMTS/LTE: problems with TMSI
Sometimes things are more complex
  Every real network is composed of multiple eNBs tuned on different channels
    For handling mobility
    For increasing capacity
  This can happen if jamming a single eNB:
    (but the majority of terminals do not really move to different eNB)
MS
2662.5 MHz
1820 MHz
806 MHz
MS
2662.5 MHz
1820 MHz
806 MHz
?

## Slide 29: IMSI catcher
Is it really feasible?
  Yes, and with simple and cheap hardware/software
  Rogue eNB:
    Opensource software like OpenAirInterface, or srsLTE
    Software Define Radio (SDR) hw, like ettus B210, BladeRF etc
  Jammer:
    Again with SDR sending signals that overlap with LTE signalling

## Slide 30: Can network self-protect against IMSI-C?
User-assisted detection of rogue base station
  measurement reports: UE→network
    include security-related values
  network will then understand if there is any IMSI-C
3GPP specification 33869
  “Study on Security aspects of Public Warning System”
    Define criteria and good practice for protecting network against false Base Stations
Bottom line:
  As of today... nothing to do against IMSI catchin

## Slide 31: What will happen with 5G
As usual, the IMSI catching problem stems from bad design
  No cryptographic problems!
What about 5G:
  IMSI1 never exchanged in the clear
  UE encrypts its ID with asymmetric cryptography
    Only network can decrypt UE’s ID
      H. Khan, B. Dowling, and K. M. Martin, “Identity Confidentiality in 5G Mobile Telephony Systems”, International Conference on Research in Security Standardisation, Nov. 2018, Darmstadt (DL).
1 In 5G IDs are called differently, check SUCI/SUPI

## Slide 32: What will happen with 5G/2
Still, something is buggy in the stack
  Protocol downgrade will be possible also with UE initially registered with 5G!
    Simple modification to the attack scheme:
MS
eNB
MS
rogue
eNB
eNB
MS
rogue
eNB
gNB
gNB
5G
4G
downgrade to LTE
gNB
5G
gNB
5G
jamming
5G
jamming
LTE&5G
4G
4G
4G
4G